ASSIGNMENT- 3

SUBJECT:-ESE-2014
GROUP - 3

Submitted By
Ankitkumar Patel – C0747455
Ronakkumar Sharma – C0747019
Dixaben Shah- C0748229

Problem:- A speech signal with bandwidth of 4 kHz is sampled at 8 kHz. The signal is corrupted by sinusoids with frequencies 1 kH, 2 kHz, and 3 kHz.
1. Design an IIR filter using notch filter components that eliminates these sinusoidal signals.
2. Choose the gain of the filter so that the maximum gain is equal to 1 and plot the log-magnitude response of your filter.
3. Load the handel sound file in OCTAVE and add the preceding three sinusoidal signals to create a corrupted sound signal. Now filter the corrupted sound signal using your filter and comment on its performance.

Solution:-

    Step 1:- Define Input signal (BW=4KHz and 8KHz sampling rate)
    Step 2:- Define noise signals of 1KHz,2KHz and 3KHz.
      Step 3:- Use Pole Zero placement method to implemet IIR-Notch Filter.
      Step 4:- Plot input signal with Noise.
      Step 5:- Plot Filtered signal(i.e original input signal filtered by IIR-notch).

Octave Code

clc;
close all;
clear all;

% define the sampling frequency
fs = 8000;
BW = 4000;
f1 = 1000;
f2 = 2000;
f3 = 3000;

% define time vector
t = 0:1/fs:1;

% define the speech signal
speech = sin(2*pi*4000*t);

% define the 3-noise signals
noise = sin(2*pi*f1*t) + sin(2*pi*f2*t) +sin(2*pi*f3*t);

% 3-notch filter section to filter-out noise from signal
r=1-BW/fs*pi; % the required magnitude of the poles

% Notch filter with a notch frequency of 1000 Hz
theta1=f1/fs*360*pi/180; %the center frequency to obtain the angle of the pole location
K1=(1-2*r*cos(theta1)+r^2)/(2-2*cos(theta1)); % the unit-gain scale factor
b1=K1*[1 -2*cos(theta1) 1] % coefficients for the numerator
a1=[1 -2*r*cos(theta1) r^2] % coefficients for the denominator
% Notch filter with a notch frequency 2000 Hz
theta2=f2/fs*360*pi/180; %the center frequency to obtain the angle of the pole..
K2=(1-2*r*cos(theta2)+r^2)/(2-2*cos(theta2)); % the unit-gain scale factor
b2=K1*[1 -2*cos(theta2) 1] % coefficients for the numerator
a2=[1 -2*r*cos(theta2) r^2] % coefficients for the denominator
% Notch filter with a notch frequency of 3000 Hz
theta3=f3/fs*360*pi/180; %the center frequency to obtain the angle of the pole.
K3=(1-2*r*cos(theta3)+r^2)/(2-2*cos(theta3)); % the unit-gain scale factor
b3=K1*[1 -2*cos(theta3) 1] % coefficients for the numerator
a3=[1 -2*r*cos(theta3) r^2] % coefficients for the denominator

b=conv(conv(b1,b2),b3); %convolution for the numerators
a=conv(conv(a1,a2),a3); %convolution for the denominators
y=filter(b,a,speech); % filtering Signal with Noise
subplot(2,1,1);
plot(t,speech+noise); % Input Signal with noise

grid on;
xlabel('Normalized Frequency');
ylabel('Magnitude');
title('Input Signal with Noise ');
subplot(2,1,2);
plot(t,y); %Filtered Signal at 1000Hz, 2000Hz, and 3000Hz

grid on;
xlabel('Normalized Frequency');
ylabel('Magnitude');
title('Filtered Signal without Noise ');

Output